Issue : 1	           FTR-G1/G2  Relay Specification         Automotive Relay

[FEATURES]

- Smallest package for automotive relay in the world.

- Compact for high density packaging. (67% volume of previous generation FTR-P3/P4)

- Both single relay and twin relay available.

- High contact capacity with proven contact material. (100K operations, 14VDC, 25A achieved, even with reduced size)

- Coil power savings (640mW nominal achieved with state-of-the-art magnetic analysis/design)

- Semi-quiet relay (average acoustic noise level: 56dB distance 5cm)

- Typical applications

- Wiper, Power window, Door lock, Sunroof, Power seat, Interior lighting etc.

- Features                                           : Lead-free and cadmium-free contacts as green product

- Sealed type

- ORDERING INFORMATION

[EXAMPLE]   FTR-G1   C    N    012    WA

(a)        (b)  (c)    (d)    (e)

- Series Name			: FTR-G1; single relay,  FTR-G2; twin relay

- Contact Arrangement	          C : 1 form C

- Coil Sensitive		          N : Contact gap min. 0.2mm

- Coil Number			: Nominal Voltage

- Contact Material		       WA	: Silver Alloy

- COIL DATA CHART

  - Chart 1

| Coil Number | Nominal Voltage [VDC] | Coil Resistance [ohms] (tolerance of 10% at 20 deg ) | Operate Voltage [VDC] (at 20 deg) | Release Voltage [VDC] (at 20 deg) | Nominal Power [mW] (tolerance of 10% at 20 deg) |
| --- | --- | --- | --- | --- | --- |
| 009 010 012 | 9 10 12 | 127 156 225 | 5.5 6.3 7.3 | 0.75 0.9 1.0 | 640 |

- SPECIFICATIONS

| Item | FTR-G1CN( )WA FTR-G2CN( )WA |
| --- | --- |
| Contact | Arrangement | 1 Form C (1 Form C x 2) |
|  | Material | Silver alloy |
|  | Style | Single |
|  | Resistance (initial) | Max. 100 mohms (at 1A 6VDC) |
|  | Rating | 25A 14VDC |
|  | Max. Carrying Current | 25A / 1hour (at 25ºC, 100% rated coil voltage) |
|  | Max. Inrush current | 35A |
|  | Max. Switching Current | 35A at 16VDC |
|  | Min. Switching Load | 1A 5VDC |
| Coil | Nominal Power (at 20ºC) | 630 mW |
|  | Operate Power (at 20ºC) | 237 mW |
|  | Operating Temperature | -40ºC to +85ºC (no frost) |
| Time Value | Operate (without diode) | Max. 10ms (at nominal voltage, without bounce) |
|  | Release (without diode) | Max. 5ms (at nominal voltage, without bounce) |
| Insulation | Resistance (at 500VDC) | Min. 100Mohms |
|  | Dielectric Strength | B/T contacts | 500VAC, 1 minute |
|  |  | B/T coil and contacts | 500VAC, 1 minute |
| Life | Mechanical | 1x107 operations minimum |
|  | Electrical | 1x105 ope. min. 25A 14VDC (locked motor load) |
| Vibration Resistance | Miss Operation | 10 to 55 Hz at double amplitude of 1.5mm |
|  | Endurance | 10 to 55 Hz at double amplitude of 1.5mm 10-500 Hz 45m/s2 |
| Shock Resistance | Miss Operation | Min. 100m/s2 (11(1ms) |
|  | Endurance | Min. 1,000m/s2 (6(1ms) |

4. Schematics (Bottom View)

FTR-G1 series: Single type               FTR-G2 series: Twin type

5. PC board mounting hole layout (Bottom View)

FTR-G1 series: Single type               FTR-G2 series: Twin type

- DIMENSIONS

FTR-G1 series: Single type

FTR-G2 series: Twin type