FTR-B3-RF Relay

■FEATURES

●Excellent high frequency characteristics up to 1GHz (Impedance 50 ohm)

by specialized shield structure.

●Between contacts capacitance　:　0.1pF (10MHz)

●Surface mounting type ( Insertion mounting type available )

●Ultra miniature flat package saves space.

(Height 6.7mm, Mounting area 97mm2  / Reduced the area to 42% of

that of UM1 relay）

●Low consumption power  :  Standard type　140mW  (24V: 230mW)

Latching type    100mW  (24V: 120mW)

●High reliability  :  bifurcated contacts

■SPECIFICATIONS

●Contact Rating	:  10V,10mADC  1W (1GHz)

●Contact Arrangement	:  2  Form C, 1 Form A

●Consumption Power   : 100mW~230mW

●High Frequency Characteristics  ( Impedance 50 ohm,  ~1GHz )

・Isolation		: Between open contacts  30dB     ( 2 Form C type )

35dB     ( Bypass type )

40dB     ( 1 Form A type )

Between contact sets      40dB     ( 2 Form C type )

・Insertion loss	: 0.3dB　( 2 Form C type)

0.4dB   ( Bypass type)

0.5dB   ( 1 Form A type)

・V.S.W.R.		: 1.2

●Between contacts capacitance	: 0.1pF　(10MHz)

■COIL DATA CHART

● Standard Type

| Nominal voltage [VDC] | Coil resistance [ohm](±10%) | Must operate voltage [VDC] | Must release voltage [VDC] | Nominal power [mW] |
| --- | --- | --- | --- | --- |
| 1.5 | 16.1 | 1.13 | 0.15 | 140 |
| 3 | 64.3 | 2.25 | 0.3 | 140 |
| 4 | 114 | 3 | 0.4 | 140 |
| 4.5 | 145 | 3.38 | 0.45 | 140 |
| 6 | 257 | 4.5 | 0.6 | 140 |
| 9 | 579 | 6.75 | 0.9 | 140 |
| 12 | 1028 | 9 | 1.2 | 140 |
| 24 | 2504 | 18 | 2.4 | 230 |

● Single Winding Latching Type

| Nominal voltage [VDC] | Coil resistance [ohm](±10%) | Must operate voltage [VDC] | Must release voltage [VDC] | Nominal power [mW] |
| --- | --- | --- | --- | --- |
| 1.5 | 22.5 | 1.13 | 1.13 | 100 |
| 3 | 90 | 2.25 | 2.25 | 100 |
| 4.5 | 203 | 3.38 | 3.38 | 100 |
| 6 | 360 | 4.5 | 4.5 | 100 |
| 9 | 810 | 6.75 | 6.75 | 100 |
| 12 | 1440 | 9 | 9 | 100 |
| 24 | 4800 | 18 | 18 | 120 |

■DIMENSIONS

● Dimensions                                                                                                      ● Suggested mounting pad

(Top view)

● Schematics

(Top view)

(1) 2 Form C type　　                                                   (2) 1 Form A type

(3) Bypass type

1) N.C Bypass type　　　　　　　　　　     　　2) N.O Bypass type

*1   Pin No.4 and Pin No.7 short circuit by external connection. Use Pin No.5 and Pin No.6 for signal switching.

*2   Pin No.3 and Pin No.8 short circuit by external connection.

*3   Pin No.5 and Pin No.6 short circuit by external connection.

■REFERENCE DATA – High Frequency Characteristics

Sample relay  :  Coil nominal voltage 4.5V type

Measuring condition :  Impedance 50 ohm

# Text boxes

Ultra miniature flat package.

High frequency signal switching.

Bypass

2Form C

1Form A

Bypass

● V.S.W.R.

1Form A

Bypass

2Form C

● Insertion loss

● Isoration

2Form C

(Open contacts)

2Form C

(Contact sets)

*1

Isolation

35dB (1GHz)

Insertion loss

0.4dB(1GHz)

Insertion loss

0.4dB(1GHz)

Isolation

35dB (1GHz)

Isolation

30dB (1GHz)

Insertion loss

0.3dB(1GHz)

Isolation

40dB (1GHz)

Insertion loss

0.5dB(1GHz)

*3

*2

(Unit  : mm)

1Form A